## Slide 1
Indian institute of technology bombay
Ctara
(technology and development)
Final Presentation
on
Evaluation of UAV-based high resolution and
satellite based medium resolution canopy images with
ground based LAI for citrus crop stress
h
by
j
Rahul Raj (143350008)
Project Guide
Prof. J. Adinarayana, CSRE

## Slide 2
8.8 tons / Ha
22-35 tons / Ha
Source: agricoop.nic.in: Department of Agriculturecooperation, and farmers welfare, India
Image Source: http://www.imgoz.com/ Image Source: Worldatlus
Image source: UNDP
Image Source: http://www.mapsofworld.com/
Average
Yield
Citrus fruit industry: Third largest fruit industry of India (Source: NHB)
846000 ha land under citrus crop cultivation in India (Source: Department of Agriculture, GOI)
Issue ???
Problem Identification

## Slide 3
Problem Identification
Reasons of Low Yield
Soil fertility / Nutrients requirement temperature aberration
Pest/Disease Limitations with traditional knowledge of citrus cultivation
Lack of Advance technology Water stress etc. etc. etc.
Mostly due to
Disease like Gummosis, Water stress, lack of advance technology and limitations of traditional knowledge and other biotic & abiotic pressure
Which is result of
Unscientific Farm Management
(unable to understand relations between various factors)

## Slide 4
The Study Area

## Slide 5
Village Name | Benoda | Goregaon | Bargaon | Nagziri
Geo location of test site | 21º27’4’’N 78º11’23’’E | 21º25’41’’N 78º9’38’’E | 21º26’16’’N 78º8’0’’E | 21º26’55’’N 78º 9’9’’E
The Study Area
Area majorly affected by Gummosis and Fruit drop.
Other identifiable disease are Root-rot, fruit splitting, fruit canker.
4.7 km
2.5 km
2.5 km
8.5 km
Benoda
Nagziri
Bargaon
Goregaon
Warud

## Slide 6
The Study Area
Root-rot
Fruit Canker
Gummosis

## Slide 7
Sub-meter resolution satellite image | Drone based high resolution image
Cloud cover and atmospheric dust particles create bottleneck on quality of imaging | NO effect of cloud cover or atmospheric dust particles on captured images
Getting images for civilian purpose takes at least 1 week. | Images can be obtained in hours depending on size of the farm.
Images captured at some fixed time of day depending on frequency of revolution of satellite. | Images can be captured at desired time of day.
Maximum available Panchromatic geometrical resolution is 30 cm while Multispectral resolution would be 1.24m. | Geometrical resolution may go around 1 cm.
Minimum area map which can be ordered is 25 square km or more. (if only natural colour map required then 10 square km) | Map can be generated for small targeted area which would be much cheaper than satellite imaging.
Images generally taken with angle making 0 degree with vertical. | Images at different angle can be taken which will help in getting architectural information of Orchards.
Source1: http://www.landinfo.com/satellite-imagery-pricing.html
Source2: http://www.satimagingcorp.com/satellite-sensors/geoeye-2/
Source3: only natural colour map: http://cms.mapmart.com/Products/SatelliteImagery/AvailableImmediately.aspx
Source3: http://rami-benchmark.jrc.ec.europa.eu/
Platform Selection

## Slide 8
Selection of Drone
Sr. No | Fixed Wing | Multi Rotor
1 | Needs direct human handling for taking off | No need of direct human handling for taking off
2 | Requires landing stripe for safe landing | Can land in small area, No need of landing stripe
3 | Unstable in windy condition | Relatively more stable in windy condition
4 | Can’t be stopped during flight | Can be stopped during flight
5 | Flight speed is relatively high and thus can cover more distance in same time | Flight speed is relatively low
6 | Can’t take sharp turns during flight | Can take sharp turns during flight
Quad-copter is selected
300 gram payload: 15 mints flight time
Collaboration with “DronaAviation”

## Slide 9
Digital image collection using UAV platform
High density LAI meter data collection using LAI meter
Image Stitching and geo-tagging to make orthomosaic
Determination of LAI from gap fraction
Identification of the equation which correlates between two LAI values taken from drone and LAI meter
Comparison of UAV, Google and LAI meter data
Google images
Process flow Diagram

## Slide 10
Selection of Camera
Digital Point and Shoot Camera
16 MP programmable camera
Focus at infinity
Programmed to capture images at every 3 seconds

## Slide 11
Image Capturing Technique
Source: http://drones.newamerica.org/
Source: http://www.mdpi.com/
70 % frontal overlap
50 % side overlap
@ 30 m height, image capture speed 1 per 3 sec then UAV speed should be less than 3.4 m/sec (considering FOV 60º)

## Slide 12
Field implementation
Figure: Field implementation is done after proper permission from Police.
Figure: Using LAI meter in plot of Nagziri

## Slide 13
Camera FOV is 30° and 24°
Average image size 9 MB
Average pixels per square cm is 3
Resolution

## Slide 14
Leaf Area Index
The ratio of leaf surface to soil surface is termed leaf area index
Leaf area is important input parameters in canopy photosynthesis modelling
                …….Humboldt University of Berlin
Monitoring distribution and changes of LAI is important for assessing growth and health of vegetation ……Food and Agriculture organisation
LAI measurement
Figure: use of LAI meter in farm
Figure: Drone using which images are captured
16 MP Digital Point and Shoot programmable camera
Focus at infinity
Programmed to capture images at every 3 seconds
LAI meter | Drone based top of the canopy Image
Time consuming and labour intensive method | Time saving and least human labour
LAI Values are highly dependent on handling and position of the LAI meter | Top of canopy images are same for a plot and gives a unique output data after processing
Ignore reading when its B reading becomes more than A (reference) value | Number of pixels with different grayscale levels should be enough to form Gaussian curve

## Slide 15
Place: Nagziri, Warud Taluka, Amravati, Maharashtra
High resolution (3cm * 3cm) citrus farm map
(made from images captured by drone)
LICOR’s LAI 2200 is used to read LAI values in farm by moving in Ro to R22 rows
Rows extraction from the map
(depending on position of LICOR data)
- - - - - - - - - - - - - - - - - - - - - - - - - - - -
R0 R1 R19 - - - R22

## Slide 16
Extracted Rows
Total number of Rows – 23 (20 rows are valid)
In Rows 6, 15 and 22 Licor meter couldn’t read LAI values
22
15
06
Note: Star marked Rows i.e. 06, 15 and 22 are not used

## Slide 17
Image Block extraction from the Rows
(depending on position of LICOR data)
Total valid image blocks: 71
Row 7
Image blocks separated from Row 7

## Slide 18
Image Processing
How to get LAI from canopy image
Source: Paper on “Retrieval of leaf area index from top-of-canopy digital photography over agricultural crops’ by J. Liu and E. Pattey.
P0(ϴ) : Gap fraction in view or solar zenith angle ϴ.
G(ϴ) : Foliage projection coefficient for the plane perpendicular to direction ϴ
K(ϴ) : Canopy Extinction Coefficient.
is an important point (first minima of curve) as it separates green and non green pixels. Minima is a point whose left and right side values are greater than its own value
Gap fraction is representation of density of green crop canopy. i.e. how much percentage of ground area is not covered with leaves when seen from above the canopy. Higher the gap fraction, lower the green canopy density.

## Slide 19
Separate Red, Green and Blue band image
Extraction using MATLAB
One block from Row 7
Red band image
Green band image
Blue band image

## Slide 20
Converting Greenness to grayscale image
2G – R - B
Grayscale
Greenness image
Grayscale image of Greenness
Greenness image is colored image and thus have 3 dimensions (Dimensions are X, Y and 3rd dimension shows value of R, G and B)
Grayscale version of Greenness image is having only Row and column as dimension and thus it’s histogram can easily separate number of pixels based on intensity value which is direct separation of green and non green area in the image

## Slide 21
Histogram of grayscale image and applying LPF
Low Pass Filter

## Slide 22
LAI values of Licor & Gap fraction of images
(Arranged in decreasing order of Licor’s LAI value)
All ‘m’ named columns has LAI values stored from Licor’s LAI meter
All ‘d’ named columns has gap fraction values calculated from digital image
Average is calculated using k = 0.5

## Slide 23
Gap fraction of images
Vs
LAI of images
&
LAI of Licor

## Slide 25
LPF applied on actual values

## Slide 26
Row | Google map LAI | Licor LAI
0 | 1.099132904 | 1.32
1 | 1.099132904 | 2.66
2 | 1.7512575 | 2.34
3 | 1.831581714 | 2.26
4 | 0.662849991 | 0.79
5 | 0.445037493 | 3.21
11 | 0.464368592 | 2.56
12 | 1.010681387 | 1.58
16 | 8.930816487 | 1.06
18 | 8.930816487 | 1.49
19 | 1.102253841 | 1.49
20 | 0.646204035 | 1.63
21 | 0.646204035 | 1.09
Google image based LAI value Vs LAI meter data
Scatter plot
Values are weakly negatively correlated with
LAI values can’t be determined for small areas as no sufficient pixels are available in small area of google map
2943

## Slide 27
Google image based LAI value Vs Drone data
Scatter plot
Values are weakly correlated with
LAI values can’t be determined for small areas as no sufficient pixels are available in small area of google map

## Slide 28
Summary / Conclusion
Drone based method of finding LAI seems promising as the values are strongly correlated with LAI meter values.
Drone based LAI values are more consistent at given location, as in top of the canopy images, visible gap fraction is constant but in case of LAI meter, the visible gap fraction depends on orientation of the LAI stick and can change even for centimeter shift in any direction.
Google map based LAI values are not correlated with any of the other two methods due to its low resolution.

## Slide 29
Future scope
Presence of green non-leafy part in top of the canopy image (presence of green grass in canopy background) creates bottleneck in finding actual gap fraction which further results in wrong LAI estimation. Research can be done on removing any non-leafy area from top of the canopy images.
To see effect of different seasons on LAI, such research work should be carried out in other seasons too.
Temporal collection of top of the canopy images can give information about changes in canopy structure over time which can be further correlated with yield estimation.
LAI values can be associated with NDVI values to estimate the level of healthiness of the crop.

## Slide 30
THANK YOU